Jay A. Greenwell, PLS, LLC

Land Surveying and Land Planning

34 Wayne Ave.

Suffern, NY 10901

(845) 357-0830

email: greenwellpls@aol.com

VILLAGE OF UPPER NYACK -- AMENDED CHAITIN SITE PLAN

February 22, 2023

The subject property has been the subject of numerous Planning Board and ZBA meetings, lasting over many years, and this current application seeks to formalize several existing conditions.

- There is an existing steep and unstable slope condition at the westerly side of the property which has impacted the adjoining uphill owners and needs to be remedied. This was caused by the original construction of the house and the construction activity that extended beyond the original proposed limit of disturbance. It is proposed to construct a retaining wall and add fill to the westerly slope area to reduce the potential for continued erosion.

This action will require Planning Board approval for disturbance to slopes in excess of 40%.

- During the course of construction and over the years of living in this location, the owner / applicant has installed various walks, walls, patio areas, etc. that accrue towards development coverage beyond that permitted by the code. Originally, this lot was subject to the R-2 code, which allowed a maximum of 25%. A prior variance permitted 27.4%. The coverage variance was exacerbated by the new maximum permitted R-30 coverage limit of 20%, as well as the new slope area deductions.

This required a variance for maximum development coverage of 39.4% (which would be 23.3% based on the gross lot area of 44,694 sf). That variance was granted in July of 2022.

- Subsequent to the construction of the house, the owner / applicant installed stone pillars with an entrance gate and lights on top of the pillars. The height of the pillars was approved by the ZBA on 12/17/13 to be 8’ high vs. the permitted maximum of 6’. However, the west pillar is 7.8 feet high and the east pillar is 8.7 feet high, due to the pitch of the road. The height of the pillars has been determined by the Village to include the lighting on top, making the total assembly 11.75 feet high. The gate is 9.25’ high.

This variance from the maximum height allowed of 6 feet for walls and fences was also granted in July of 2022.

As to the request to the Planning Board for the disturbance to steep slopes, the resulting grades will benefit the uphill owners by mitigating the existing sharp drop-off at the rock cliff at the westerly property line. The construction of a retaining wall and additional fill will raise the grade, making the slope at the boundary line less steep, as demonstrated by the cross sections prepared by Sound Engineering Associates, LLC and submitted herewith.

This will also benefit the homeowner by the establishment of a stable uphill area that will not be as susceptible to erosion over the years.

Construction of the wall and softening of the grade will require cooperation of the uphill owners (Clemensen and Sinnott) and the applicant’s attorney has been in touch with those owners to secure permission to work on the easterly portion of their lands.